## Slide 1: Introduction to Mininet / POX / Pyretic
December 2017
In the name of Allah

## Slide 2: What Will We Talk About?
Introduction
Mininet
  Installation
  Basic Commands
  Mininet with default controller
POX Controller
  Installation
  Layer 2 Learning Switch
  Spanning Tree Switch
  Exercise 1
Pyretic language
  Installation
  Example
  Exercise 2

## Slide 3: SDN Philosophy

## Slide 4
SDN Philosophy

## Slide 5: Mininet
Get Started With Mininet:
  Mininet VM Installation
  Installation from Packages
  Native Installation from Source
    git clone git://github.com/mininet/mininet
    cd mininet
    git tag
    git checkout 2.2.2
    cd ..
    mininet/util/install.sh

## Slide 6: Creating First Network with Mininet 
sudo mn --topo tree,depth=2,fanout=8 --test pingall
$ sudo mn -c
Start a minimal topology and enter the CLI:
  mininet> help
  mininet> nodes
  mininet> net
  mininet> dump
  mininet> xterm h1 h2
Mininet’s API in Python

## Slide 7: Mininet’s API in Python
from mininet.topo import Topo
from mininet.net import Mininet
  class DCTreeTopo(Topo):
  def build(self):
    CoreSwitch1 = self.addSwitch('s1’)
    AggSwitch1 = self.addSwitch('s' )
    self.addLink(CoreSwitch1,AggSwitch1,bw=100, delay='5ms')
    host1 = self.addHost('h1')
    self.addLink(host1, EdgeSwitch1,bw=10, delay='15ms')
  if __name__ == '__main__':
  topo = DCTreeTopo(k)
  net=Mininet(topo) net.addController(name='c0',controller=RemoteController,ip='127.0.0.1',port=6633)
  net.start()
  CLI(net)
  net.stop()

## Slide 8: Useful Utility
iperf:
  Iperf is a tool to measure the bandwidth and the quality of a network link.
  On server side (h2 for example):
    # iperf –s
  On client side (h1 for example):
    # iperf –c 10.0.0.2

## Slide 9: Controllers Suitable for Mininet

## Slide 10: POX Controller
$ sudo mn --controller=remote, ip=[controller IP], port=[controller listening port]
Getting the Code / Installing POX
  $ git clone http://github.com/noxrepo/pox
  $ cd pox
Invoking POX
  ./pox.py forwarding.l2_learning

## Slide 11: Hub Behavior
root@Ubuntu:# mn --topo single,3 --controller=remote,ip=127.0.0.1,port=6633
mininet> xterm h1 h2 h3
root@ubuntu:~/pox# ./pox.py forwarding.hub
In the xterms for h2 and h3, run tcpdump, a utility to print the packets seen by a host:
  # tcpdump -XX -n -i h2-eth0
  # tcpdump -XX -n -i h3-eth0
In the xterm for h1, send a ping:
  # ping -c1 10.0.0.2
Now, see what happens when a non-existent host doesn't reply.
  # ping -c1 10.0.0.5

## Slide 12: pox/forwarding/l2_learning.py
The launch function
  def launch (transparent=False, hold_down=_flood_delay):
  core.registerNew(l2_learning)
A Class with Component name:
  class l2_learning (object):
    def __init__ (self, transparent):
      core.openflow.addListeners(self)
      self.transparent = transparent
    def _handle_ConnectionUp (self, event):
        LearningSwitch(event.connection, self.transparent)

## Slide 13: LearningSwitch
class LearningSwitch (object):
  def __init__ (self, connection, transparent):
  self.connection = connection
  self.transparent = transparent
  self.macToPort = {}
  def _handle_PacketIn (self, event):
    def flood (message = None):
    def drop (duration = None):
    self.macToPort[packet.src] = event.port # 1

## Slide 14: Packet_In Handler
if packet.dst.is_multicast:
flood()
else:
if packet.dst not in self.macToPort:
flood()
else:
port = self.macToPort[packet.dst]
if port == event.port:
drop()
return

## Slide 15: Packet_In Handler
msg = of.ofp_flow_mod()
msg.match=of.ofp_match.from_packet(packet, event.port)
msg.idle_timeout = 10
msg.hard_timeout = 30
msg.actions.append(of.ofp_action_output(port = port))
msg.data = event.ofp
self.connection.send(msg)

## Slide 16: POX APIs
Working with POX: The POX Core object
  from pox.core import core
Working with Addresses: pox.lib.addresses
  from pox.lib.addresses import IPAddr, IPAddr6, EthAddr
  ip = IPAddr("192.168.1.1")
Events With Multiple Listeners
  specifying priority in addListener() or addListeners()
  halting events

## Slide 17: OpenFlow Events & Messages
ConnectionUp
ConnectionDown
PacketIn
packet_out
flow_mod

## Slide 18: Pyretic Language
Existing SDN controllers offer programmers a low-level programming interface akin to assembly language.
We present Pyretic, a programming platform that raises the level of abstraction and enables the creation of modular software, allowing programmers to create sophisticated SDN applications.
Pyretic encourages programmers to focus on how to specify a network policy at a high level of abstraction, rather than how to implement it using low-level OpenFlow mechanisms.

## Slide 19: Network Policy as a Function
Building the Pyretic VM
Install Python dependencies
Patch asynchat Python dependency
Install git subtree
Clone the pyretic repository to your home directory
Setup your environment variables EITHER by adding the following lines to end of .profile
https://github.com/frenetic-lang/pyretic/wiki/Building-the-Pyretic-VM

## Slide 20: Parallel and Sequential Composition
match(dstip=’2.2.2.8’) >> fwd(1)
match(switch=1) >> match(dstip=’2.2.2.8’) >> fwd(1)
L = match(dstip=’1.2.3.4’) >>
((match(srcip=’0.0.0.0/1’)>> modify(dstip=’2.2.2.8’)) +
(-match(srcip=’0.0.0.0/1’)>> modify(dstip=’2.2.2.9’)))
L=match(dstip=’1.2.3.4’) >>if_(match(srcip=’0.0.0.0/1’),
modify(dstip=’2.2.2.8’),modify(dstip=’2.2.2.9’))

## Slide 21: The Exercises Explanation
Access Control Module in POX Controller
Firewall Module in Pyretic

## Slide 22: Other Codes & Commands
sudo apt-get update
sudo apt-get upgrade
sudo apt-get install python
sudo apt-get install git
ssh mininet@192.168.206.137
export pythonpath=$home/pyretic:$home/mininet:$home/pox
chmod 777 –r .
scp my_firewall.py mininet@192.168.206.137:pyretic/pyretic/modules

## Slide 23: Email: z330.sasan@gmail.com || High Speed Networks Lab